Machine

WALL (WT AssembLy Language) is a Machine Simulator coupled with a custom Assembly Language.
The Machine consists of a Memory Table, Program Status Word, Registers, Clock, Display Console, Disassembled Console, and a Memory Error Console.
# Memory Table
The Memory Table is a visual collection of WALL’s memory (RAM). WALL possess 2^8 bytes of memory (256 bytes). Memory is a non-circular “array” of addresses beginning at address 0 and ending at address 255.
- Memory Cell
  - Contains a hexadecimal value of 1 byte from 00 to FF
  - Address 255 (FF) is a reserved address for WALL.
    - No user values may be placed into it.
    - No instructions can be placed into it.
    - The Stack begins at this address and grows into descending memory
# Clock
The action mechanism of WALL. The Clock operates in a 3 step cycle – Fetch, Decode, and Execute.
- Fetch
  - Fetches the instruction from the Instruction Register
- Decode
  - Validates and reads the instruction
- Execute
  - Takes the decoded instruction and executes it, altering Registers and Memory.
# Program Status Word
WALL’s PSW consists of two special registers. These registers maintain the current state of the machine.
- Instruction Pointer
  - Points to the memory address of the next instruction to be executed
- Instruction Register
  - Contains the content of the currently executing memory cell
  - Possesses the byte code of the currently executing instruction.
# Registers
WALL has 14 General Purpose Registers and two Reserved Registers. These registers are used by the programmer to do quick arithmetic and movement on memory content.
- General Purpose Registers
  - R0: Comparison Register
    - Whenever a comparison needs to occur, then the “compare against” value needs to be loaded into this register.
  - RF: Display Register
    - Anything loaded into this register will be displayed into the Display Console in it’s ASCII equivalent value.
  - All other GPRs have no specialized use.
- Reserved Registers
  - RD (RBP): Base Pointer Register
    - Used by the Machine/Programmer to mark the location of the current Base of the Stack
  - RE (RSP): Stack Pointer Register
    - Used by the Machine/Programmer to mark the location of the current Top of the Stack
# Display Console
Takes the value loaded into RF and displays the ASCII character that is equivalent to the hexadecimal value. Gives visual feedback to the programmer.
# Disassembled Console
Takes the content of Six memory addresses, centered on the Instruction Register, and displays them in their Assembler Language format.
# Memory Error Console
Displays Run-Time errors to the user.
- Address Overflow
  - Address is greater than maximum Address
- Reserved Address
  - Address 255 is reserved by WALL
- Boundary Fault
  - IP is pointing to a odd address – non-fatal error
# Call Stack
A top-down stack that shows basic information of each CALL instruction that was executed.